## Slide 1: Electricity and Electric Fields
Electric Charge and Electric Field
Notes: Photo by <a href="https://stockcake.com/i/electronic-copper-rivers_2144812_1306062">Stockcake</a>

## Slide 2: Electricity and Electric Fields
Static Electricity and Electric Charge
Coulomb's Law and Electric Fields
Electric Circuits and Ohm’s Law

## Slide 3: Learning Objectives
Describe the flow of electric charge in a circuit.
Use Ohm’s Law to calculate voltage, current, and resistance.
Analyze series and parallel circuits.
Calculate electrical power in simple circuits.
Apply Coulomb’s Law to determine electric forces between charges.
Describe and calculate electric field strength.
Interpret electric field diagrams.

## Slide 4: Electricity and Electric Fields
Static Electricity and Electric Charge
Coulomb's Law and Electric Fields
Electric Circuits and Ohm’s Law

## Slide 5: What is Electric Charge?
Protons carry a positive charge, electrons carry a negative charge, and neutrons are neutral. It’s important to remember that like charges repel, while opposite charges attract.
Notes: Images: https://www.bbc.co.uk/bitesize/articles/zshqqfr#z7rbbqt

## Slide 6: Electric Charge
Electric charge comes in two types: positive and negative.
The charge of a proton is exactly equal in magnitude (but opposite in sign) to the charge of an electron.
The fundamental unit of electric charge (the charge of a single proton or electron) is approximately
A Coulomb is a very large amount of charge – it’s equal to the charge accumulated from electrons.
Notes: https://theengineeringmindset.com/how-electricity-works/
The charge carried by a proton is exactly the opposite of that carried by an electron.
The SI unit for electric charge is the coulomb (abbreviated as “C”)
The fundamental unit value of charge is 1.602×10-19 C.

## Slide 7: Electricity and the atom
Notes: https://theengineeringmindset.com/how-electricity-works/

## Slide 8: Static Electricity
Buildup of electrons on an object
Happens on insulators (charges can’t move)
“Static” = not moving
Caused by friction (e.g., carpet)
Can cause sparks, attraction

## Slide 9
https://youtu.be/Dn78UMpcZF4?feature=shared
Notes: https://youtu.be/Dn78UMpcZF4?feature=shared
What Is Static Electricity? - KS3 Physics (BBC Bitesize)
~2min

## Slide 10: Conductors and Insulators
Notes: https://www.vedantu.com/evs/poor-conductors-of-electricity

## Slide 11
https://youtu.be/qZjDMQbn3a0?si=QoOpNLYx2j2biNbl
https://youtu.be/qZjDMQbn3a0?si=QoOpNLYx2j2biNbl
Notes: https://youtu.be/qZjDMQbn3a0?si=QoOpNLYx2j2biNbl
Electrical Conductors and Insulators
~2min 30sec

## Slide 12: Electricity and Electric Fields
Static Electricity and Electric Charge
Coulomb's Law and Electric Fields
Electric Circuits and Ohm’s Law

## Slide 13: Coulomb
Charles-Augustin de Coulomb was an 18th-century French physicist who studied the force between electric charges and formulated Coulomb’s Law, earning his name as the unit of electric charge.

## Slide 14: Coulomb’s Law

## Slide 15: Coulomb’s Law
The value of the electric constant, also known as the vacuum permittivity, F/m
Notes: The value of the electric constant, also known as the vacuum permittivity \epsilon_0, is:
\epsilon_0 = 8.85 \times 10^{-12} \, \text{F/m} \quad (\text{farads per meter})

## Slide 16
Vacuum permittivity tells you how well the vacuum can “permit-tivity” an electric field. The unit farad per meter (F/m) comes from how ε₀ appears in electrostatic equations, particularly in Coulomb’s law and in equations involving capacitance.
A farad is the SI unit of capacitance:
1 farad = the ability to store 1 coulomb of electric charge per volt.
So it measures how easily electric charge can be stored.
When we say vacuum permittivity is in F/m, we mean:
How much “capacitance‑like behavior” the vacuum can provide per unit distance.
This comes from the formula for a parallel-plate capacitor:
where:
is capacitance (farads)
is plate area (m²)
is separation (m)
So ε₀ must have units of F/m for the equation to work dimensionally.
Notes: This is an FYI slide to explain more

## Slide 17
Shuffling on carpet as an example typically involves 1 to 10 microcoulombs.
That’s enough to create a spark you can see and feel (especially in dry air), but it’s not dangerous—just startling.
A lightning bolt typically transfers 5 to 25 coulombs.
That’s about a billion times more charge than a carpet zap!
It flows through the air in a huge current (10,000–100,000+ amps) for a very short time.
Microcoulomb vs a Coulomb

## Slide 18
https://youtu.be/TFlVWf8JX4A?si=zHIAAfBWb61Qf4io
~10 min optional
Notes: https://youtu.be/TFlVWf8JX4A?si=zHIAAfBWb61Qf4io
Electric Charge: Crash Course Physics #25
~10 min though optional if want and have time/attention

## Slide 19: Electric Fields
An electric field is a region of space around a charged object where other charges experience a force.
The electric field points away from positive charges and toward negative charges.
Notes: https://www.electroniclinic.com/introduction-to-electric-field-definition-and-formula/
https://courses.lumenlearning.com/suny-physics/chapter/18-5-electric-field-lines-multiple-charges/

## Slide 20: Electric Field Defined
*The test charge q0 is always assumed positive. Direction of E is the direction of force on a positive test charge.
Notes: Electric field is defined using a positive test charge
Q is the source charge and q is the “other one” we are investigating
Field lines always point in the direction of the force acting on a positive test charge
We drop the q_0 because it’s just a tool to probe the field and doesn’t affect the field’s value

## Slide 21: Magnetism
Earth acts like a giant magnet, with its magnetic south pole near the geographic North Pole. This causes the north pole of a magnet to point north, which is how it got its name. Similarly, the south pole of a magnet points toward Earth's geographic South Pole.

## Slide 22: Electricity and Electric Fields
Static Electricity and Electric Charge
Coulomb's Law and Electric Fields
Electric Circuits and Ohm’s Law

## Slide 23: Voltage
Voltage, also called electric potential difference, is the energy per unit charge provided by an energy source, such as a battery. It represents the push that drives electric charges through a circuit. Voltage is measured in volts (V).
Notes: https://openstax.org/books/physics/pages/18-4-electric-potential

## Slide 24: Current
Electric current represents the rate at which electric charge flows and is measured in amperes (A), with one ampere equal to one coulomb of charge passing a fixed point per second.

## Slide 25: Resistance
Resistance is a measure of how much a material opposes the flow of electric current. Materials with low resistance, such as metals, allow current to flow easily, while materials with high resistance, such as rubber or glass, inhibit current flow. Resistance is measured in ohms (Ω)

## Slide 26: Ohm’s Law
Ohm’s Law describes the relationship between voltage, current, and resistance in an electric circuit. It is given by:
• V is the electric potential difference (V)
• I is the current in amperes (A)
• R is the resistance in ohms (Ω)

## Slide 27
https://youtu.be/QZt0wPlQSQE?si=RceakXs3OszJFAG4
~6min Optional
Notes: https://youtu.be/QZt0wPlQSQE?si=RceakXs3OszJFAG4
What is Ohms Law: definition, formulas, triangle, demonstration
~6min Optional if needed

## Slide 28: Basic Circuits
A simple circuit in TinkerCad
https://www.tinkercad.com/

## Slide 29: Schematic Symbols

## Slide 30
Notes: https://makeabilitylab.github.io/physcomp/electronics/schematics.html

## Slide 31: Series Circuit
Series Circuit: Components are connected end-to-end so that the same current flows through each part.
Schematic Diagram: A simplified, symbolic drawing that shows how components are connected in a circuit, using standardized symbols.
Notes: https://www.physicsclassroom.com/class/circuits/Lesson-4/Circuit-Symbols-and-Circuit-Diagrams

## Slide 32: Parallel Circuit
Parallel Circuit: Components are connected across common points or junctions, forming multiple paths for current to flow.
Each component is connected directly across the power source, so each receives the full voltage.
Notes: https://www.physicsclassroom.com/class/circuits/Lesson-4/Circuit-Symbols-and-Circuit-Diagrams

## Slide 33: Tinkercad Tinker Example

## Slide 34: Don’t Burn Out the LED!
A Light Emitting Diode (LED) can tolerate a maximum current of around 20 mA.
There are two resistors in series as shown in the diagram. What should the total resistance be to light the LED without burning it out?
What combination of resistors, in Ohms (Ω), would you use to build the circuit?

## Slide 35: Use Ohm’s Law
Total resistance:

## Slide 36: Select Resistors
Add two resistors in series that’ll add up to an effective resistance of about 450 or so ohms.
Why is it fine to use a little bit more resistance than that which we calculated?
Recall the 4-band color code chart:
  Band 1 → first digit
  Band 2 → second digit
  Band 3 → number of zeros
300 Ohms
160 Ohms
Notes: Bad Boose Rots Our Young Guts But Vodka Goes Well

## Slide 37: Resistor Color Code Chart

## Slide 38
https://youtu.be/Dq6zbNWB0VI?si=VhoW-_D0PZKmyjW-
~5 min optional
Notes: https://youtu.be/Dq6zbNWB0VI?si=VhoW-_D0PZKmyjW-
Series & Parallel Circuits
~5 min optional

## Slide 39
Notes: Photo by <a href="https://stockcake.com/i/steampunk-sunset-city_1908216_1281623">Stockcake</a>